## Slide 1
Introductory Flow Cytometry
J. Paul Robinson & John Nolan

## Slide 2
4-Cellular Immunophenotyping
Slides originally developed by Carleton C. Stewart, Ph.D. & Sigrid J. Stewart
John P. Nolan
Scintillon Institute
San Diego, CA
jnolan@scintillon.org
Short Course

## Slide 3: Immunophenotyping is one of the major applications of flow cytometry in both the clinical and research environment
It involves
Using antibodies conjugated to fluorescent probes to tag cells
Combining size (scatter) and granularity (side scatter) as additional parameters
Using multiparameter analysis to determine individual cell types
Looking for rare cell populations
Plotting the various types of cells

## Slide 4
Some Slides originally developed by Carleton C. Stewart, Ph.D. & Sigrid J. Stewart
Slide from commercial brochure

## Slide 5: Advanced Immunophenotyping
Slide from commercial brochure

## Slide 6: Advanced Immunophenotyping
Slide from commercial brochure

## Slide 7: Advanced Immunophenotyping
Slide from commercial brochure

## Slide 8
Kf
Kr
Ab + Ep AbEp
Kf range is usually ~ 106
Kr range is usually ~ 10-3
Ka = Kf/Kr = 106/10-3 = 109
Kf =
AbEp
Ab
Ep
Kr =
AbEp
Ab
Ep
THE LAW OF MASS ACTION
Notes: The Fab binding site on an antibody combines with its epitope, the three dimensional site on the antigen, according to the law of mass action. K1 is the forward (or association) rate constant and K2 is the reverse (or disassociation) rate constant. These reactions are concentration dependent reactions and the concentration of the antibody epitope (AbE), free antibody (Ab) and free epitope (E) can be determined at equilibrium by the equation.
For “good” antibodies the concentration required for association can be several orders of magnitude higher than that of “bad” antibodies’. Non-specific binding occurs at higher immunoglobulin concentrations than for “good” antibody binding but may be similar in concentration to “bad” antibody binding concentration. This latter condition means that non-specific binding cannot be distinguished from specific binding.

## Slide 9
Notes: The hallmark of specific binding is by ligand/receptor interaction kinetics and it is saturable according to the law of mass action. Fc receptor binding, often erroneously called non-specific binding, is actually very specific binding. Non-specific immunoglobulin binding involves weaker electrostatic forces due to protein /protein interactions. Thus, every protein inside or on the surface of a cell has the potential of non-specifically binding immunoglobulins. We will use the word “antibody” when we speak of specific binding and “immunoglobulin” when we speak of non-specific binding.

## Slide 10
Specific Activity is the concentration
of bindable antibody to its epitope
divided by the protein concentration.
2
[F(ab')
]
SA =
(protein)
Notes:   While the specific activity of antibody preparation has never been provided, it is by far the most important quality assessment parameter. This single number provides the user an objective assessment of the amount of specific antibody to the total amount of immunoglobulin in the preparation. This number is high for “good” antibodies and low for “bad” antibodies.

## Slide 11: Reasons Antibodies do not bind to cells:
overconjugation
not purified
degradation of binding site
aggregation
Notes: This list shows how “good” antibodies can be turned into “bad” antibodies. The result is that the concentration of “good” antibody to total immunoglobulin is low. Only the antibody can bind to its epitope, but the immunoglobulin can bind non-specifically to all proteins on the cell.

## Slide 12
STORING OF ANTIBODIES :
Proteases destroy antibodies in:
• ascitic fluid
• serum
• bacteria
Use sodium azide
Use highly purified albumin or gelatin
as carrier
Purify antibodies immediately
Notes: Antibodies are very stable proteins if properly stored. Proteases are the enemy of antibodies because they degrade it into lower molecular weight immunoglobulin fragments that do not bind to their eptiope. This causes an increase in the concentration of immunoglobulin fragments and a concommitant decrease in “good” antibody, resulting in a decrease in specific activity and an increase in non-specific binding.

## Slide 13
SPECIFIC
ANTIBODY
NON-SPECIFIC
ANTIBODY
CONCENTRATION
AMOUNT BOUND
TITERING ANTIBODIES
Notes: As the concentration is increased more antibody binds to the epitope until near saturation occurs to produce a sigmoid curve, when the amount bound is plotted as a function of the concentration. The titer, therefore, is the lowest concentration needed to produce near saturation and is determined as the posterior side of the inflection of the binding curve. Non-specific binding, however, occurs at a higher concentration, but does not reach saturation because the concentration of the protein target is so high.

## Slide 14
3
3 µg
s/n = 2.5
1 µg
s/n = 2.1
0.3 µg
s/n = 2.4
0.1 µg
s/n = 4.1
0.03 µg
s/n = 4.8
0.01 µg
s/n = 4.6
0.003 µg
s/n = 3.5
0.001 µg
s/n = 3.2
auto
Notes: To determine the titer, target cells are stained with various dilutions of antibody and the mean channel fluorescence of positive and negative cells determined. The marker may be set using an isotype control or unstained cells (auto). It is shown here as the change from black to red. The ratio of the mcf of the positive cells to negative cells is calculated. We call this the signal to noise ratio (s/n). Because each antibody, when properly titered, is its own isotype control, there is no need to use a separate one.

## Slide 15
8
7
6
5
4
3
2
1
0
2
3
4
5
Dilution
Signal to Noise
TITER
Notes: By plotting s/n as a function of the concentration an inverted parabolic shaped curve is produced whose zenith is the titer. This concentration produces the best distinction between positive and negative cells. The left side of the curve represents rapid changes in non-specific binding and a slow change in specific binding. The right side reflects decreased saturation of epitopes by antibody.

## Slide 16
10
1
10
2
10
3
10
4
10
1
10
2
10
3
10
4
10
1
10
2
10
3
10
4
1 µg S/N
Ab 278
IC 5.8
isotype
control
antibody
cytokeratin
.3 µg S/N
Ab 100
IC 3.6
10
1
10
2
10
3
10
4
.01 µg S/N
Ab 25.7
IC 2.6
number
Notes: Because the protein targets for non-specific binding are orders of magnitude higher inside cells than on the surface membrane, non-specific binding needs to be evaluated independent of and in parallel to specific binding. To do this, an isotype control immunoglobulin is matched in concentration to the test antibody. Dilutions of both are prepared and permeabilized target cells are stained with each. The s/n is again computed, as before, as the ratio of cells stained with antibody to cells stained with the isotype control.

## Slide 17
6
5
4
3
2
1
0
0
10
20
30
40
50
60
Dilution
Signal to Noise
TITER
Notes: The titer at maximum signal to noise rato is determined for intracellular antigens in the same manner as surface staining. Unfortunately, many antibodies show no zenity at all. For example, reaction product may be easily seen under a microscope, but no positive to negative discrimination is found by flow cytometry if the antibody binds uniformily to proteins throughout the cell causing dim fluorescence as a background. Since the flow cytometer integrates fluorescence, some of this dim fluorescence may be much greated than the integrated sum of the bright reaction spots. Thus, antibodies that may work well in an immunohistochemical mode may not work at all in flow cytometry.

## Slide 18
10
4
10
4
10
1
10
2
10
3
10
4
10
1
10
2
10
3
10
4
PE-CD4
TC-CD8
10
1
10
2
10
3
10
1
10
2
10
3
FITC-CD3
number
10
1
10
2
10
3
10
4
10
1
10
2
10
3
10
4
VERIFICATION OF ANTIBODY COMBINATIONS
Notes: Once the titer has been determined, antibodies can be combined for multiparameter immunophenotyping. It must be determined that the antibodies do not interfere with one another and that after combining they are still at the proper titer. Remember, antibody binding is concentration dependent, therefore, the volume of each antibody will dilute the other antibodies, potentially causing them to be below titer when combined. To test the combination, each antibody is used separately to stain cells but, to a final tube, the combination is added to target cells. The histogram for each single antibody is produced and the histogram for the combination is overlayed and compared. They should match within limits established by the laboratory. In this example, CD3 and CD8 is only slightly different and well within the acceptable limit while CD4 is a perfect match.

## Slide 19: BLOCKING IS IMPORTANT

## Slide 20
INDIRECT IMMUNOFLUORESCENCE STAINING
NO BLOCKING
Primary Antibody:
Second Antibody:
murine monoclonal
fluoresceinated
antibody
goat anti-mouse
IgG F(ab')
2
Fab
epitope
FcR
A
B
C
D
Fc
Notes: To block immunoglobulin binding to Fc receptors the cells are incubated with a high concentration of IgG. Purified IgG must be used because serum sources are totally inadequate as the IgG concentration in serum is not high enough. Fc receptor binding also obeys the law of mass action. An adequate concentration of IgG is 200 µg/ml per million leukocytes. This is approximately ten times that found in normal serum. If cells are not blocked, the antibody can bind to either the epitope or the Fc receptor, as shown. In the suspension of equal cell populations shown, 75% of the cells would be positive, but only 50% express the desired epitope.

## Slide 21
ISOTYPE CONTROL- myeloma protein
AUTOFLUORESCENCE CONTROL
E
F
G
H
Notes: When the isotype control is used, it binds to the Fc receptor, but not to the epitope. Therefore, 50% of cells are positive. It is common to subtract the percentage of positive cells in the isotype control from that found for the antibody. Therefore this would result in an erroneous 25% net positive cells because epitope positive and Fc receptor positive cells have been subtracted from the total. The practice of subtracting an isotype control is not recommended.

## Slide 22
BLOCKING WITH GOAT IgG
goat IgG
Notes: The selection of the proper IgG for blocking is very important and will be discussed in more detail. When a second conjugated antibody is used with a primary antibody, the block must be from the same species from which the second antibody was made. When biotinylated or directly conjugated antibodies are used, we recommend using mouse IgG.

## Slide 23
add Mab
Fab
add fluoresceinated goat anti-mouse IgG F(ab')2
Notes: When Fc receptors are blocked first, there is no Fc receptor binding by the specific antibody. This can be confirmed by comparing isotype control binding to unstained cells. The antibody now binds only to its epitope to provide the correct percentage of positive cells.

## Slide 24
VERIFICATION OF BLOCK
1. FcR and non-specific binding
FL-MAB + PE-mIgG
2. gIgG + FL-MAB + PE-mIgG
Notes: PE - mIgG can bind to FcR on leukocytes and this can be demonstrated by staining cells with a FL-MAB and PE-mIgG (1). If goat IgG is added to the cells (2) first, in high concentration, so that all FcR are occupied, addition of PE-mIgG no longer binds to the FcR.

## Slide 25
EFFECT OF BLOCKING ON ANTIBODY BINDING TO MONONUCLEAR CELLS
LOG FLUORESCENCE
CELL VOLUME
Notes: Human mononuclear cells were incubated with FITC-CD3 without blocking (top) or incubated 10 min. with an IgG block (bottom). Note that the IgG effectively blocked Fc receptor binding to monocytes.

## Slide 26
number
TOTAL
A
B
C
D
channel number
Notes: Murine peritoneal macrophages were incubated with 1 µg of FITC labeled IgG. In A, no block was used. In B, 1 µg of IgG, in C, 3 µg and in D, 10 µg of IgG was added to macrophages 10 min before staining. Note how blocking is a concentration dependent reaction. Since 1 µg or less of antibodies is used to stain cells, note that 10 times as much IgG is required to saturate the Fc receptors.

## Slide 27: DEAD CELLS CAN BE A PROBLEM
They bind antibodies non-specifically
They masquerade as specific subsets
They cause data misinterpretation

## Slide 28: ANTIBODIES BIND NON-SPECIFICALLY TO DEAD CELLS
FL-KAPPA
PE-LAMBDA
dead cells
ALL CELLS
VIABLE CELLS
A
B
Notes: In A, a population of kappa positive, lambda positive B-cells is shown. If the suspension is stained with ethidium monoazide (which freely crosses the membrance of dead cells and stains the DNA but is effectively excluded from live cells) live cells can be explicitly evaluated. As shown in B, elimination of dead cells also eliminates thekappa positive, lambda positive population, providing an objective evaluation of this lambda positive B-cell malignancy.

## Slide 29: ONE COLOR IMMUNOPHENOTYPING
RPCI
LFC

## Slide 30
STRATEGIES IN MULTICOLOR FLOW CYTOMETRY
RPCI
LFC

## Slide 31
CELLULAR ANTIGENS
Adhesion
Receptors
Metabolic
cytokines
structure
enzymes
courtesy of Jim Bender
Notes: In the most recent leukocyte typing workshop over 160 antibodies were classified into defined groups. These antibodies bind to cytokines or chemokine receptors, sensory molecules, cytokine or chemokine ligands, metabolic proteins, adhesion molecules, enzymes, structural proteins and other important functional proteins within the cell. These antibodies can be used to identify specific cell subsets by their unique repertoire of molecular expression as well as their functional state using multiparameter flow cytometry.

## Slide 32
FLOW CYTOMETRY VS MICROSCOPIC IMAGING

## Slide 33: FOUR COLOR SINGLE LASER IMMUNOPHENOTYPING
Antibodies labeled with fluorescein
Antibodies labeled with phycoerythrin (PE)
Antibodies labeled with PE/Texas Red
Antibodies labeled with PE/CY5 or PerCP

## Slide 34: FOUR COLOR DUAL LASER IMMUNOPHENOTYPING
Antibodies labeled with fluorescein
Antibodies labeled with phycoerythrin (PE)
Antibodies labeled with PE/CY5 or PerCP
Antibodies labeled with APC, CY5 or CY7

## Slide 35
CD3
CD3
CD3
CD56
CD56
CD8
FOUR COLOR PATTERN
CD4
CD8
CD56
CD8
CD4
CD4
Notes: As additional antibodies are combined, further subsetting can be achieved and heretofore unknown populations of cells discovered (CD3+CD4+CD8-CD56+). The increased dimensionality of data may make its visualization difficult.

## Slide 36: VISUALIZING EACH POPULATION
BIVARIATE DOT PLOTS CAN BE USED TO DISPLAY THE PATTERNS GENERATED BY MULTIPARAMETER DATA.
FL1
FL4
FL2
FL4
FL3
FL4
FL1
FL3
FL2
FL3
FL1
FL2
4 COLOR
3 COLOR
2 COLOR
Notes: We use color to visualize the cell populations resolved by multiple antibodies. When two antibodies are used, the populations can be displayed in a single bivariate distribution. When 3 antibodies are used there are 3 possible bivariate displays, resulting in 8 separate populations and when 4 antibodies are used there are 6 bivariate combinations and 16 possible populations. If a population is colored in one bivariate display, its location in the other displays can be easily seen.

## Slide 37: UNDERSTANDING BINARY LOGIC IS USEFUL
Note that in binary logic the 1st parameter is sequenced as -/+, two parameters as --/++, 3 parameters as ----/++++, etc.. for as many parameters that are measured. The problem encountered after 3 parameters is...how does one visualize the multiple populations?

## Slide 38
A
b
2
A
b
1
A
b
3
A
b
3
A
b
2
A
b
1
A
b
1
A
b
2
A
b
3
c
o
l
o
r
A
b
1
A
b
2
A
b
3
c
o
l
o
r
ne
eg
.
(
-
)
n
e
g
.
(
-
)
n
e
g
.
(
-
)
g
r
e
y
n
e
g
.
(
-
)
n
e
g
.
(
-
)
p
o
s
.
(
+
)
r
u
s
t
o
s
.
(
+
)
n
e
g
.
(
-
)
n
e
g
.
(
-
)
y
e
l
l
o
w
p
o
s
.
(
+
)
n
e
g
.
(
-
)
p
o
s
.
(
+
)
b
l
u
e
ne
g
.
(
-
)
p
o
s
.
(
+
)
n
e
g
.
(
-
)
c
y
a
n
n
e
g
.
(
-
)
p
o
s
.
(
+
)
p
o
s
.
(
+
)
v
i
o
l
e
t
no
s
.
(
+
)
p
o
s
.
(
+
)
n
e
g
.
(
-
)
g
r
e
e
n
p
o
s
.
(
+
)
p
o
s
.
(
+
)
p
o
s
.
(
+
)
r
e
d
COLOR PATTERNS USED TO VIEW COEXPRESSION
Notes: When three antibodies are used together the eight possible combinations of positive and negative cells are shown in the table. When a unique color is assigned to each combination, the position of cells with the same properties generate patterns in the three bivariate plots, representing all the combinations.

## Slide 39
Boolean Logic Table For Four Color Immunophenotyping
Notes: When more than 3 antibodies are used, 16 colors are required. Now there is a practicle problem because we cannot distinguish more than 10 colors with the printers currently used by most flow cytometry labs. A strategy to circumvent this problem is to use 8 colors twice. One antibody is selected as a gating antibody: 3 bivariate distributions using 8 colors for positive cells, for that antibody, and 3 additional bivariate distributions, using the same 8 colors, for negative cells are displayed.

## Slide 40
A
B
C
D
E
F
Ab1
Ab1
Ab1
Ab1
Ab1
Ab1
Ab2
Ab2
Ab2
Ab2
Ab2
Ab2
Types of Antigen Expression
Notes: There are several patterns of antigen expression. The interpretation of them is important for describing the meaning of co-expression. In A, Ab2 is uniformly expressed, while Ab1 is co-expressed by Ab2 cells in a heterogeneous manner. In B, Ab1 is uniformly expressed, while Ab2 is co-expressed by Ab1 cells in a heterogeneous manner. In C, a population of Ab1+Ab2- cells is found, but it is the Ab2+ cells that exhibit heterogeneous expression to produce the Ab1+Ab2+ population. Thus, Ab1 cells are not positive for Ab2. In D, there are two distinct populations: Ab2+Ab1- and Ab2+Ab1+, while in E, the two populations are Ab1+Ab2- and Ab1+Ab2+. In F, correct interpretation can be difficult because this pattern is exhibited by highly autofluorescent cells that are Ab1-Ab2- or dead cells that non specifically bind Ab1 and Ab2. If it is either of these two situations, all combinations of antibodies used will show this pattern on the same percentage of cells. If this pattern represents a true subpopulation of cells it will be unique to the one antibody combination.

## Slide 41
Notes: Interpreting Co-expression: The pattern of expression of two or three markers provides the means for assignment of co-expression. The possibilities are illustrated in this Figure. The antibody combination CD7CD19CD2 was used and in A, B and C the same specimen is shown. CD19 is homogeneously expressed on the cells, as shown in A, but CD7 is expressed in a heterogeneous manner, as shown by a continuum of CD7 expression from negative (cyan) to positive (green). Thus, a proportion of the CD19+ cells express CD7. In B, a small population of CD19+CD2+ cells (violet) is shown. This could be heterogeneous expression of CD2 on the CD19 population, a distinct subset that expresses both markers, or an artifact. Because of this uncertainty, when the frequency of cells co-expressing two or more markers is small, and because the level of confidence increases with increased frequency, we have set a threshold of 10% above which we designate co-expression as real and below which it is uncertain. In this case, the frequency was below 10% of the CD19+ population and we do not know its significance. In C, a distinct subset of CD7+CD2+ cells (blue) is shown which do not express CD19 (A and B): these are normal T-cells. Using a specimen from another patient, in D, non-specific binding is often characterized by events on a 45 degree angle (red) as the antibodies bind equally to all cells. Populations exhibiting this pattern are not included in the interpretation even though they may be greater than 10%.

## Slide 42: Non-specific Binding to Monocytes
A
B
C
PerCP-CD4
PE-CY5-CD4
FSC
SSC
CD25
CD25
Notes: The PE-CY5 tandem complex binds specifically to myelomonocytic cells. This can result in the misinterpretation of immunophenotypic data using these reagents. In this illustration CD4 binding to monocytes is shown in A, but the PE-CY5 tandem can also bind to monocytes, causing them to appear as bright as lymphocytes (in B).

## Slide 43: EFFECT OF BATCH VARIATION
PE-fluorescence
Notes: Because there is no industry wide standard for producing tandem complexes, the amount of compensation required will be dependent on the supplier. This can severly compromise immunophenotyping because each company’s reagent will have to be separately compensated. In some cases a different lot of reagent from the same company may require a completely different amount of compensation. Unless properly used, these reagents can produce artifactual, misinterpreted data.