## Slide 1
Advanced Flow Cytometry
J. Paul Robinson & John Nolan

## Slide 2: Multiplexed Analysis of Soluble Analytes
John P. Nolan
Scintillon Institute
San Diego, CA
jnolan@Scintillon.org
Short Course

## Slide 3: Learning Objectives
  Microparticle-based molecular analysis
  Multiplexed encoding of microparticles
  Applications
    Immunoassay
    Nucleic acid analysis
    Molecular interactions

## Slide 4: Beads in Flow Cytometry
Alignment
Calibration
Quantification
Compensation
Solid supports for molecular analysis

## Slide 5: Microsphere-based Molecular Assembly
microsphere
Immobilization Fluorescent labels
DNA: avidin-biotin, covalent synthetic, enzymatic
Protein: affinity tags chemical, expressed
Lipid: adsorption, self assembly synthetic, enzymatic
Glycan: avidin-biotin, covalent synthetic

## Slide 6: Multiplexing Microspheres
Multiple colors
  Luminex
  Becton Dickenson
Size and color
  QuantumPlex – Polysciences
  Cytoplex – Duke Scientific
  Sphero - Spherotech
Size
  Many, do it yourself

## Slide 7: Multiplexed Assay Concept

## Slide 8: Throughput Advantages
100 X 90 = 9000 = 100 X 90

## Slide 9: Instruments
Dedicated Bead Reader
  Luminex 100 (BioPlex, LiquiChip, etc)
Multipurpose
  BD FACSArray
  Any flow cytometer

## Slide 10: Multiplexed Analysis Methods
Immunoassays
  Multiplexed ELISAs
Nucleic Acid Analysis
  Soluble DNA chips
Molecular Assembly and Screening
  Basic research
  Drug discovery

## Slide 11: Immunoassay

## Slide 12: Capture Considerations
Antibody: Affinity, specificity
  Good monoclonals
Immobilization: Stability, sensitivity
  Physical adsorption
  Protein G
  Covalent attachment
Pierce

## Slide 13: Capture Bead Characterization
Labeled analyte
  Active binding sites
  Affinity of capture
Labeled antibody
  Immobilized antibody
Fluorogenic protein stain
  Immobilized protein

## Slide 14: Reporter Considerations
Antibody: Affinity and specificity
  Good monoclonal, distinct epitope
  ELISA antibody pairs
Labeling
  Direct fluorescence, OK for wash protocols
  Biotin/fluorescent avidin, best for no wash

## Slide 15: Washing
Centrifugation + resuspension
  Cumbersome for large numbers of samples; loss of beads due to clumping, sticking
Filtration
  Better for large scale apps; blocking
Magnet
  Should be good
None
  Faster processing; higher backgrounds

## Slide 16: Immunoassay Protocols
Step | Protocol A | Protocol B
1 | Sample + beads (4°C overnight) | Sample + beads (RT, 2 hours)
2 | Wash 2x | Fluorescent reporter (RT, 30 min)
3 | Biotinylated reporter Ab (RT, 1 hour) | Wash
4 | Fluorescent streptavidin (RT, 30 min) | Measure
5 | Wash 3x | 
6 | Measure | 

## Slide 17: Data Analysis
Linear fit (log-log)
4 Parameter logistic fit (semilog)
5 parameter logistic fit
Kellar and Douglass (2003) J Immun Meth

## Slide 18: Immunoassay Summary
Multiplexed assays provide comparable sensitivity to conventional ELISA assays
Greatly improved throughput and sample use efficiency
Many kits commercially available
Protocols for assay development well established

## Slide 19: Genetic Analysis
Sequence Detection: Is it there?
  Pathogen detection – Yes or No
Sequence Analysis: A or T, or C, or G
  Disease diagnostics
  Gene mapping
Sequence Abundance: How much is there?
  Gene expression
    Relative: increase/decrease relative to control
    Absolute: moles or moles/L

## Slide 20: Capture Considerations
DNA immobilization
  Physical adsorption: glass beads
  Covalent conjugation: EDC of amino oligos
Target
  Oligonucleotides
  Single stranded DNA
  Double stranded DNA

## Slide 21: Reporter Considerations
Oligonucleotide hybridization
Nucleotide incorporation
Direct Labeling
Indirect Labeling
Amplification

## Slide 22: Nucleic Acid Analysis
Hybridization

## Slide 23: Nucleic Acid Analysis
Single Base Extension

## Slide 24: Gene Expression (mRNA)
Plex Set 1003: ABCB1, ABCB4, ABCB11, ABCC1, ABCC2, ABCC3, ABCG2, GAPDH, SLC22A1, SLC22A7
Plex Set 1006: CCL2, CSF2, CX3CL1, GAPDH, ICAM1, IL6, IL8, PTGS2, SELE, VCAM1
Plex Set 1007: AICDA, CD19, CD40, CD80, CD86, FAIM3, GAPDH, ICAM1, LTA, RIPK4
Plex Set 1010: ACTB, B2M, GAPDH, HPRT1, PGK1, RPLP0
Plex Set 1011: GAPDH, GBP1, IFIT1, IFITM1, IRF1, ISG20, MX1, OAS1, PRKRA, TNFAIP3
Plex Set 1018: ABCB1, ABCB11, ABCC2, ACTB, CDKN1A, CYP1A2, CYP2B6, CYP2C9, CYP3A4, GAPDH, IFNG, IL1B, IL8, IL10, PPIB, TNF, TNFSF6, VEGF
Plex Set 1019: EBI3, GAPDH, HPRT1, IFNG, IL1A, IL1B, IL6, IL6R, IL6ST, IL12A, IL12B, IL12RB1, IL12RB2, IL15, IL17, IL17F, IL17R, IL17RC, IL18, IL23A, IL23R, IL27, IL27RA, LTA, LTB, PPIB, SDHA, TNF, TNFRSF1A, TNFRSF1B
Plex Set 1024: BAD, BAK1, BAX, BCL2, BCL2L1, PPIB
Plex Set 1025: ABCA1, ABCB1, ABCB4 , ABCB11, ABCC2 , ABCC3 , ABCC4 , ABCG2, GAPDH, HNF4A, KEAP1, NCOA1, MPP1, MPV17, NFE2L2 , NR0B2 , NR1H3 , NR1H4 , NR1I2 , NR1I3 , NR3C1 , NR5A2 , PPARA, PPARGC1A , RXRA, SLC10A1, SLCO1A2, SLCO1B1 , SLCO1B3 , TCF1
Plex Set 1026: AHR, ALAS1, ALAS2, CEBPA, CEBPB, CYP1A2, CYP2B6, CYP2C9, CYP2C19, CYP2D6, CYP2E1, CYP3A4, CYP3A5, CYP3A7, CYP4A11, CYP7A1, GAPD, PPARG, UGT1A1, UGT1A4, UGT1A6, UGT1A9, UGT2A3, UGT2B4, UGT2B7, UGT2B10, UGT2B15, UGT2B17, UGT2B28, UGT3A1
Plex Set 1035: ACTB, CCL2, CCL3, CCL4, CCL5, CCL11, CSF2, CSF3, CXCL9, CXCL10, GAPDH, IFNG, IL1B, IL2, IL4, IL5, IL6, IL7, IL8, IL10, IL12A, IL12B, IL13, IL17, IL18, LTA, PPIB, TGFB1, TNF, VEGF
Plex Set 1037: ACTB, AHR, CYP1A2, CYP1B1, CYP2A6, CYP2B6, CYP2C9, CYP2C19, CYP3A4, CYP3A5, CYP4A11, GAPDH, NR1I2, NR2I3, PPARA
Plex Set 1039: ABCA1, ABCG1, CD36, FABP4, GAPDH, PPARG, PPIB, RXRA, SCARB1
Ebioscience Quantiplex

## Slide 25: microRNA Detection
Lu et al (2005)

## Slide 26: Microsphere-based Molecular Assembly
microsphere
Immobilization Fluorescent labels
DNA: avidin-biotin, covalent synthetic, enzymatic
Protein: affinity tags chemical, expressed
Lipid: adsorption, self assembly synthetic, enzymatic
Glycan: avidin-biotin, covalent synthetic

## Slide 27: Nucleic Acid Analysis Summary
Kits and reagents becoming available
Oligonucleotides provide numerous opportunities for high-level multiplexing and signal amplifciation
Many potential configurations of caputer oligos, reporter probes, amplification: application-specific

## Slide 28: Summary
Optically-encoded beads enable multiplexed solid phase assays
Sandwich immunoassays
Nucleic acid-based assays
Any molecular assembly or interaction

## Slide 29: Protocols and More Info
Chapter 1 Flow Cytometry Instrumentation
Chapter 2 Image Cytometry Instrumentation
Chapter 3 Safety Procedures and Quality Control
Chapter 4 Molecular and Cellular Probes
Chapter 5 Specimen Handling, Storage, and Preparation
Chapter 6 Phenotypic Analysis
Chapter 7 Nucleic Acid Analysis
Chapter 8 Molecular Cytogenetics
Chapter 9 Studies of Cell Function
Chapter 10 Data Processing and Analysis
Chapter 11 Microbiological Applications
Chapter 12 Cellular and Molecular Imaging
Chapter 13 Multiplexed and Microparticle‐Based Analyses
  Introduction
  UNIT 13.1 Multiplexed Microsphere-Based Flow Cytometric Immunoassays
  UNIT 13.2 Microsphere Surface Protein Determination Using Flow Cytometry
  UNIT 13.3 Use of Microsphere-Supported Phospholipid Membranes for Analysis of Protein-Lipid Interactions
  UNIT 13.4 Multiplexed SNP Genotyping Using Primer Single-Base Extension (SBE) and Microsphere Arrays
  UNIT 13.5 BeadCons: Detection of Nucleic Acid Sequences by Flow Cytometry
  UNIT 13.6 Characterization of Nuclear Receptor Ligands by Multiplexed Peptide Interactions
  UNIT 13.7 Detection of Gene Fusions in Acute Leukemia Using Bead Microarrays
  UNIT 13.8 Reagents and Instruments for Multiplexed Analysis Using Microparticles
  UNIT 13.9 Multiplexed Detection of Fungal Nucleic Acid Signatures
  UNIT 13.10 Multiplexed Analysis of Peptide Antigen-Specific Antibodies
  UNIT 13.11 Use of Flow Cytometric Methods to Quantify Protein-Protein Interactions
  UNIT 13.12 Microsphere-Based Flow Cytometry Protease Assays for Protease Activity Detection & High-Throughput Screening
  UNIT 13.13 Application of the PrimRglo Assay Chemistry to Multiplexed Bead Assays
  UNIT 13.14 Flow Cytometry of Extracellular Vesicles: Potential, Pitfalls, and Prospects
  UNIT 13.15 Optimized MOL-PCR for Characterization of Microbial Pathogens