## Slide 1
MULTIPARAMETER
IMMUNOFLUORESCENCE
Carleton C. Stewart, Ph.D. & Sigrid J. Stewart
R
L
L
OSWE
ARK
P
L
Cancer Institute
aboratory
Flow
of
Cytometry
Department of Health, State of New York
Elm and Carlton Streets
Buffalo, New York 14263
phone: 716-648-5480
fax: 716-648-8806
email: stewart@sc3101.med.buffalo.edu

## Slide 2
ANTIBODY BINDING TO CELLS

## Slide 3
Kf
Kr
Ab + Ep AbEp
Kf range is usually ~ 106
Kr range is usually ~ 10-3
Ka = Kf/Kr = 106/10-3 = 109
Kf =
AbEp
Ab
Ep
Kr =
AbEp
Ab
Ep
THE LAW OF MASS ACTION
Notes: The Fab binding site on an antibody combines with its epitope, the three dimensional site on the antigen, according to the law of mass action. K1 is the forward (or association) rate constant and K2 is the reverse (or disassociation) rate constant. These reactions are concentration dependent reactions and the concentration of the antibody epitope (AbE), free antibody (Ab) and free epitope (E) can be determined at equilibrium by the equation.
For “good” antibodies the concentration required for association can be several orders of magnitude higher than that of “bad” antibodies’. Non-specific binding occurs at higher immunoglobulin concentrations than for “good” antibody binding but may be similar in concentration to “bad” antibody binding concentration. This latter condition means that non-specific binding cannot be distinguished from specific binding.

## Slide 4
Notes: The hallmark of specific binding is by ligand/receptor interaction kinetics and it is saturable according to the law of mass action. Fc receptor binding, often erroneously called non-specific binding, is actually very specific binding. Non-specific immunoglobulin binding involves weaker electrostatic forces due to protein /protein interactions. Thus, every protein inside or on the surface of a cell has the potential of non-specifically binding immunoglobulins. We will use the word “antibody” when we speak of specific binding and “immunoglobulin” when we speak of non-specific binding.

## Slide 5
Specific Activity is the concentration
of bindable antibody to its epitope
divided by the protein concentration.
2
[F(ab')
]
SA =
(protein)
Notes:   While the specific activity of antibody preparation has never been provided, it is by far the most important quality assessment parameter. This single number provides the user an objective assessment of the amount of specific antibody to the total amount of immunoglobulin in the preparation. This number is high for “good” antibodies and low for “bad” antibodies.

## Slide 6: Reasons Antibodies do not bind to cells:
overconjugation
not purified
degradation of binding site
aggregation
Notes: This list shows how “good” antibodies can be turned into “bad” antibodies. The result is that the concentration of “good” antibody to total immunoglobulin is low. Only the antibody can bind to its epitope, but the immunoglobulin can bind non-specifically to all proteins on the cell.

## Slide 7
STORING OF ANTIBODIES :
Proteases destroy antibodies in:
• ascitic fluid
• serum
• bacteria
Use sodium azide
Use highly purified albumin or gelatin
as carrier
Purify antibodies immediately
Notes: Antibodies are very stable proteins if properly stored. Proteases are the enemy of antibodies because they degrade it into lower molecular weight immunoglobulin fragments that do not bind to their eptiope. This causes an increase in the concentration of immunoglobulin fragments and a concommitant decrease in “good” antibody, resulting in a decrease in specific activity and an increase in non-specific binding.

## Slide 8
TITERING ANTIBODIES

## Slide 9
SPECIFIC
ANTIBODY
NON-SPECIFIC
ANTIBODY
CONCENTRATION
AMOUNT BOUND
Notes: As the concentration is increased more antibody binds to the epitope until near saturation occurs to produce a sigmoid curve, when the amount bound is plotted as a function of the concentration. The titer, therefore, is the lowest concentration needed to produce near saturation and is determined as the posterior side of the inflection of the binding curve. Non-specific binding, however, occurs at a higher concentration, but does not reach saturation because the concentration of the protein target is so high.

## Slide 10
3
3 µg
s/n = 2.5
1 µg
s/n = 2.1
0.3 µg
s/n = 2.4
0.1 µg
s/n = 4.1
0.03 µg
s/n = 4.8
0.01 µg
s/n = 4.6
0.003 µg
s/n = 3.5
0.001 µg
s/n = 3.2
auto
Notes: To determine the titer, target cells are stained with various dilutions of antibody and the mean channel fluorescence of positive and negative cells determined. The marker may be set using an isotype control or unstained cells (auto). It is shown here as the change from black to red. The ratio of the mcf of the positive cells to negative cells is calculated. We call this the signal to noise ratio (s/n). Because each antibody, when properly titered, is its own isotype control, there is no need to use a separate one.

## Slide 11
8
7
6
5
4
3
2
1
0
2
3
4
5
Dilution
Signal to Noise
TITER
Notes: By plotting s/n as a function of the concentration an inverted parabolic shaped curve is produced whose zenith is the titer. This concentration produces the best distinction between positive and negative cells. The left side of the curve represents rapid changes in non-specific binding and a slow change in specific binding. The right side reflects decreased saturation of epitopes by antibody.

## Slide 12
10
1
10
2
10
3
10
4
10
1
10
2
10
3
10
4
10
1
10
2
10
3
10
4
1 µg S/N
Ab 278
IC 5.8
isotype
control
antibody
cytokeratin
.3 µg S/N
Ab 100
IC 3.6
10
1
10
2
10
3
10
4
.01 µg S/N
Ab 25.7
IC 2.6
number
Notes: Because the protein targets for non-specific binding are orders of magnitude higher inside cells than on the surface membrane, non-specific binding needs to be evaluated independent of and in parallel to specific binding. To do this, an isotype control immunoglobulin is matched in concentration to the test antibody. Dilutions of both are prepared and permeabilized target cells are stained with each. The s/n is again computed, as before, as the ratio of cells stained with antibody to cells stained with the isotype control.

## Slide 13
6
5
4
3
2
1
0
0
10
20
30
40
50
60
Dilution
Signal to Noise
TITER
Notes: The titer at maximum signal to noise rato is determined for intracellular antigens in the same manner as surface staining. Unfortunately, many antibodies show no zenity at all. For example, reaction product may be easily seen under a microscope, but no positive to negative discrimination is found by flow cytometry if the antibody binds uniformily to proteins throughout the cell causing dim fluorescence as a background. Since the flow cytometer integrates fluorescence, some of this dim fluorescence may be much greated than the integrated sum of the bright reaction spots. Thus, antibodies that may work well in an immunohistochemical mode may not work at all in flow cytometry.

## Slide 14
10
4
10
4
10
1
10
2
10
3
10
4
10
1
10
2
10
3
10
4
PE-CD4
TC-CD8
10
1
10
2
10
3
10
1
10
2
10
3
FITC-CD3
number
10
1
10
2
10
3
10
4
10
1
10
2
10
3
10
4
VERIFICATION OF ANTIBODY COMBINATIONS
Notes: Once the titer has been determined, antibodies can be combined for multiparameter immunophenotyping. It must be determined that the antibodies do not interfere with one another and that after combining they are still at the proper titer. Remember, antibody binding is concentration dependent, therefore, the volume of each antibody will dilute the other antibodies, potentially causing them to be below titer when combined. To test the combination, each antibody is used separately to stain cells but, to a final tube, the combination is added to target cells. The histogram for each single antibody is produced and the histogram for the combination is overlayed and compared. They should match within limits established by the laboratory. In this example, CD3 and CD8 is only slightly different and well within the acceptable limit while CD4 is a perfect match.

## Slide 15
CONTROL BATCH
CONTROL BATCH
Notes: It may be necessary to make new batches of the combination over time. We generally make 100 test batches of our combinations (1 - 2 months supply). The new batch must perform identically to the old batch. This is determined by staining cells with both old and new batches using the appropriate target cells. The MCF of each antibody is determined, as shown, and be within the established limits for the laboratory. Sometimes new lots of antibody from the same supplier will be different and, in this case, new limits of acceptability will need to be established.

## Slide 16: BLOCKING IS IMPORTANT

## Slide 17
INDIRECT IMMUNOFLUORESCENCE STAINING
NO BLOCKING
Primary Antibody:
Second Antibody:
murine monoclonal
fluoresceinated
antibody
goat anti-mouse
IgG F(ab')
2
Fab
epitope
FcR
A
B
C
D
Fc
Notes: To block immunoglobulin binding to Fc receptors the cells are incubated with a high concentration of IgG. Purified IgG must be used because serum sources are totally inadequate as the IgG concentration in serum is not high enough. Fc receptor binding also obeys the law of mass action. An adequate concentration of IgG is 200 µg/ml per million leukocytes. This is approximately ten times that found in normal serum. If cells are not blocked, the antibody can bind to either the epitope or the Fc receptor, as shown. In the suspension of equal cell populations shown, 75% of the cells would be positive, but only 50% express the desired epitope.

## Slide 18
ISOTYPE CONTROL- myeloma protein
AUTOFLUORESCENCE CONTROL
E
F
G
H
Notes: When the isotype control is used, it binds to the Fc receptor, but not to the epitope. Therefore, 50% of cells are positive. It is common to subtract the percentage of positive cells in the isotype control from that found for the antibody. Therefore this would result in an erroneous 25% net positive cells because epitope positive and Fc receptor positive cells have been subtracted from the total. The practice of subtracting an isotype control is not recommended.

## Slide 19
BLOCKING WITH GOAT IgG
goat IgG
Notes: The selection of the proper IgG for blocking is very important and will be discussed in more detail. When a second conjugated antibody is used with a primary antibody, the block must be from the same species from which the second antibody was made. When biotinylated or directly conjugated antibodies are used, we recommend using mouse IgG.

## Slide 20
add Mab
Fab
add fluoresceinated goat anti-mouse IgG F(ab')2
Notes: When Fc receptors are blocked first, there is no Fc receptor binding by the specific antibody. This can be confirmed by comparing isotype control binding to unstained cells. The antibody now binds only to its epitope to provide the correct percentage of positive cells.

## Slide 21
VERIFICATION OF BLOCK
1. FcR and non-specific binding
FL-MAB + PE-mIgG
2. gIgG + FL-MAB + PE-mIgG
Notes: PE - mIgG can bind to FcR on leukocytes and this can be demonstrated by staining cells with a FL-MAB and PE-mIgG (1). If goat IgG is added to the cells (2) first, in high concentration, so that all FcR are occupied, addition of PE-mIgG no longer binds to the FcR.

## Slide 22
EFFECT OF BLOCKING ON ANTIBODY BINDING TO MONONUCLEAR CELLS
LOG FLUORESCENCE
CELL VOLUME
Notes: Human mononuclear cells were incubated with FITC-CD3 without blocking (top) or incubated 10 min. with an IgG block (bottom). Note that the IgG effectively blocked Fc receptor binding to monocytes.

## Slide 23
number
TOTAL
A
B
C
D
channel number
Notes: Murine peritoneal macrophages were incubated with 1 µg of FITC labeled IgG. In A, no block was used. In B, 1 µg of IgG, in C, 3 µg and in D, 10 µg of IgG was added to macrophages 10 min before staining. Note how blocking is a concentration dependent reaction. Since 1 µg or less of antibodies is used to stain cells, note that 10 times as much IgG is required to saturate the Fc receptors.

## Slide 24: variation in gamma 1 myeloma protein binding to macrophages
mopc myeloma protein
Notes: Isotype control immunoglobulins are extensively used as controls for inappropriate antibody binding, but do they actually perform this function? This figure illustrates the binding of 7 IgG1 myeloma proteins to murine macrophages. Since none have known specificity for epitopes on macrophages that their binding represents and since murine macrophages do not bind monomeric IgG (no receptors for IgG1) and since binding ranged from 0 to 48%, one wonders what the meaning of an isotype control is.
Myeloma proteins are abnormal immunoglobulins produced by neoplastic cells. One function of macrophages is to clear altered proteins and clearly they, better than we, recognize myeloma proteins as abnormal imunoglobulins. Monoclonal antibodies are also myeloma proteins and can behave similarly. Fortunately the companies screen them for low binding so that we can be misguided into believing we have an appropriate control. Indeed, new guidelines recommend against the use of isotype controls.

## Slide 25
Second Reagent Quality
log fluorescence
cell volume
F(ab’)2 of anti IgG
anti IgG
Notes: When a fluorochrome conjugated second antibody is used to stain the primary antibody it should always be an F(ab’)2 fragment. This is clearly shown by comparing the high degree of binding of an intact FITC goat anti mouse IgG to the F(ab’)2 fragment.

## Slide 26: DEAD CELLS CAN BE A PROBLEM
They bind antibodies non-specifically
They masquerade as specific subsets
They cause data misinterpretation

## Slide 27: ANTIBODIES BIND NON-SPECIFICALLY TO DEAD CELLS
FL-KAPPA
PE-LAMBDA
dead cells
ALL CELLS
VIABLE CELLS
A
B
Notes: In A, a population of kappa positive, lambda positive B-cells is shown. If the suspension is stained with ethidium monoazide (which freely crosses the membrance of dead cells and stains the DNA but is effectively excluded from live cells) live cells can be explicitly evaluated. As shown in B, elimination of dead cells also eliminates thekappa positive, lambda positive population, providing an objective evaluation of this lambda positive B-cell malignancy.

## Slide 28
lysed, washed
cells
+ 5 µg EMA
10 min.
18 cm.
EMA PROCEDURE
WASH, FIX, AND ANALYZE
1
3
2
Notes: We recommend the EMA procedure because the azide group can be covalently linked to DNA histones by light exposure. The suspension can then be fixed without fear of staining the cells that were viable prior to fixation.
Reference
Riedy, M. C., Muirhead, K. A., Jensen, C. P., and Stewart, C. C. THE USE OF A PHOTOLABELING TECHNIQUE TO IDENTIFY NONVIABLE CELLS IN FIXED HOMOGENOUS OR HETEROLOGOUS CELL POPULATIONS. Cytometry 12:133-139, 1991

## Slide 29: Evaluating Viability with Ethidium Monoazide
FSC
SSC
FSC
SSC
FSC
FL3-EMA
R9
% dead = 5%
R2
% dead in gate = 1%
R9
Notes: Live/dead discrimination is made by plotting FSC vs EMA fluorescence in FL3, as shown. We consider speicmens that have greater than 15% dead cells as unevaluable.

## Slide 30: ONE COLOR IMMUNOPHENOTYPING
RPCI
LFC

## Slide 31
1. IgG Block MAB wash FL-second antibody F(ab')2 wash
2. IgG Block B-MAB wash FL-Avidin wash
3. IgG Block FL-MAB wash
SINGLE COLOR IMMUNOPHENOTYPING
Notes: There are three common methods for staining cells. In 1, a primary antibody is used followed by a second fluorochrome conjugated antibody. The IgG block should be obtained from the species in which the second antibody is made. The second method is to use a biotinylated antibody followed by a fluorochrom conjugated streptavidin. The easiest method (#3) is to use a fluorescence conjugated primary antibody. For the last two, any species IgG can be used for blocking. We use mouse IgG.

## Slide 32
CORRELATED (LIST MODE) DATA ACQUISITION
Entry No.
Value
Cell Number
Parameter
1
80
1
FSC
2
100
1
SSC
3
40
1
Green
4
20
1
Red
5
90
2
FSC
6
120
2
SSC
7
100
2
Green
8
110
2
Red
-
50
n
FSC
-
75
n
SSC
-
110
n
Green
k
120
n
Red
Notes: In a flow cytometer the detectors measure photons released from fluorochromes or scatter from the laser beam and quantitatively convert this energy into electronic pulses. The height or area of the the pulse is converted into a number that is transferred to a computer file. Each number enters a list in the same order for each cell. This is called correlated list mode data. If four parameters are measured on 4,000 cells, there will be 40,000 numbers in the list. In this example the first four numbers in the list are the values of FSC, SSC, green and red fluorescence for cell number 1. The next four are for cell number 2 etc. to the nth cell.

## Slide 33: Analysis of List Mode Data
CD4 FLUORESCENCE
number of cells
forward scatter
CD4 fluorescence
A
B
C
region A
region B
region C
Notes: This figure illustrates how data is analyzed using a list mode file. In the upper left view three gaussian distributions of cells are resolved in the FSC histogram and regions A, B, and C bracket them. This specifies the range of numbers in the list mode file for the FSC parameter that will are illustrated in the other three views. When the fluorescence of region A is displayed, a population with a high fluorescence and a population with low fluorescence are found. When region B is displayed a relatively homogeneous population of cells with intermediate fluorescence is found and when region C is displayed, only cells with bright fluorescence, identical to those in region A are found. This provides a powerful means for evaluating cell subsets.

## Slide 34
STRATEGIES IN MULTICOLOR FLOW CYTOMETRY
RPCI
LFC

## Slide 35
CELLULAR ANTIGENS
Adhesion
Receptors
Metabolic
cytokines
structure
enzymes
courtesy of Jim Bender
Notes: In the most recent leukocyte typing workshop over 160 antibodies were classified into defined groups. These antibodies bind to cytokines or chemokine receptors, sensory molecules, cytokine or chemokine ligands, metabolic proteins, adhesion molecules, enzymes, structural proteins and other important functional proteins within the cell. These antibodies can be used to identify specific cell subsets by their unique repertoire of molecular expression as well as their functional state using multiparameter flow cytometry.

## Slide 36
FLOW CYTOMETRY VS MICROSCOPIC IMAGING

## Slide 37
TWO COLOR IMMUNOPHENOTYPING
Antibodies labeled with fluorescein
Antibodies labeled with phycoerythrin
RPCI
LFC

## Slide 38
TWO COLOR IMMUNOPHENOTYPING
1. IgG Block + MAB
wash
FL- second antibody F(ab')2
wash
IgG Block + PE-MAB
wash
2. IgG Block + B-MAB + FL-MAB
wash
PE-Avidin
wash
3. IgG Block + FL-MAB + PE- MAB
wash
Notes: Any of the 3 equations for single color immunophenotyping can be combined for 2 color immunophenotyping. When a primary and second antibody are combined with either a biotinylated or directly conjugated primary antibody the first staining reaction must always be the primary/secondary step, shown in #1 above. Before adding either the biotinylated or directly conjugated antibody a mouse IgG block must be performed without exception. Biotinylated and directly conjugated antibodies may be mixed together prior to staining.

## Slide 39
COMBINED INDIRECT AND DIRECT
IMMUNOFLUORESCENCE STAINING
NO BLOCKING
Primary Antibody: mMAB
Second Antibody: FGAM
PE-mMAB
Notes: This figure illustrates the problem encountered if no intervening block is performed between the indirect and direct labeling reactions. Unoccupied binding sites on the goat anti mouse IgG are free to bind the biotinylated or directly conjugated antibodies when they are added, if they are not blocked. Note that all cells with an epitope to the primary antibody will be labeled with the PE-mMab whether they have epitopes (1st cell) or not (3rd cell).

## Slide 40
NO BLOCK
CD8 + FGAM
PE-CD4
21%
6%
49%
Notes: Note all CD8 positive leukocytes have bound CD4 when an intervening block was not used between the indirect and direct staining reactions.

## Slide 41
VERIFICATION OF BLOCK
• Second Reagent Block
gIgG + MAB wash FL-GAM wash PE-mIgG
gIgG + MAB wash FL-GAM wash mIgG + PE-mIgG
Notes: A control to run in order to verify the block is effective is to add a directly conjugated isotype control antibody after blocking the indirect staining reaction. No cells should be positive for this isotype control.

## Slide 42
COMBINED INDIRECT AND DIRECT IMMUNOFLUORESCENCE STAINING
BLOCKING
Primary Antibody: mMAB
Second Antibody: FGAM
PE-mMAB

## Slide 43
BLOCKED
CD8 + FGAM
PE-CD4
42%
12%
Notes: By adding excess mouse IgG before adding directly conjugated CD4, no CD8+ CD4+ cells are found.

## Slide 44
THREE COLOR IMMUNOPHENOTYPING
Antibodies labeled with Fluorescein
Antibodies labeled with Phycoerythrin
Antibodies labeled with Tandem Complex to Avidin
Tandem Complexes are Texas Red or CY 5 coupled to Phycoerythrin
Per CP is a natural Tandem Complex of peridinin and chlorophyll a protein

## Slide 45: SINGLE COLOR HISTOGRAMS
Notes: When single antibodies are used for immunophenotyping the percentage of positive cells for each marker can be obtained. But what does one do about multiple populations revealed by the intensity of staining?

## Slide 46: TWO COLOR PATTERN
FL1-CD3
FL2-CD4
color
CD3-CD4- black
CD3+CD4- blue
CD3-CD4+ cyan
CD3+CD4+ green
Notes: Color can be used to visualize populations: when 2 antibodies are used only 4 colors are required. When antibodies are combined together a pattern emerges when bivariate histograms are displayed. The geometric clusters of events represent cells with like properties.

## Slide 47: THREE COLOR PATTERN
CD3
CD4
CD3
CD4
CD8
CD8
Notes: When more than two antibodies are combined, additional subsetting of the cells can be achieved. If one antibody is used to identify a specific lineage of cells, i.e. CD3, five subsets of T-cells are easily resolved, when CD4 vs C8 is displayed.

## Slide 48: FOUR COLOR SINGLE LASER IMMUNOPHENOTYPING
Antibodies labeled with fluorescein
Antibodies labeled with phycoerythrin (PE)
Antibodies labeled with PE/Texas Red
Antibodies labeled with PE/CY5 or PerCP

## Slide 49: FOUR COLOR DUAL LASER IMMUNOPHENOTYPING
Antibodies labeled with fluorescein
Antibodies labeled with phycoerythrin (PE)
Antibodies labeled with PE/CY5 or PerCP
Antibodies labeled with APC, CY5 or CY7

## Slide 50
CD3
CD3
CD3
CD56
CD56
CD8
FOUR COLOR PATTERN
CD4
CD8
CD56
CD8
CD4
CD4
Notes: As additional antibodies are combined, further subsetting can be achieved and heretofore unknown populations of cells discovered (CD3+CD4+CD8-CD56+). The increased dimensionality of data may make its visualization difficult.

## Slide 51
FL1
FL3
FL3
FL2
FL2
FL1
Notes: A population of cells in FL1 vs FL2 has been colored red. These cells could be anywhere along the projection of FL2 on to the FL3 axis or FL1 on to the FL3 axis.

## Slide 52
FL1
FL1
FL2
FL2
FL3
FL3
Notes: When the cells are displayed in the FL2 vs FL3 bivariate plot, two distinct populations are found: FL1+FL2+FL3- and FL1+FL2+FL3+. When displayed in the FL1 vs FL3 bivariate plot we see these two populations are again spacially separated. By displaying each bivariate plot with similar axis side by side, the appropriate projections can be made, shown by the parallel lines.

## Slide 53: VISUALIZING EACH POPULATION
BIVARIATE DOT PLOTS CAN BE USED TO DISPLAY THE PATTERNS GENERATED BY MULTIPARAMETER DATA.
FL1
FL4
FL2
FL4
FL3
FL4
FL1
FL3
FL2
FL3
FL1
FL2
4 COLOR
3 COLOR
2 COLOR
Notes: We use color to visualize the cell populations resolved by multiple antibodies. When two antibodies are used, the populations can be displayed in a single bivariate distribution. When 3 antibodies are used there are 3 possible bivariate displays, resulting in 8 separate populations and when 4 antibodies are used there are 6 bivariate combinations and 16 possible populations. If a population is colored in one bivariate display, its location in the other displays can be easily seen.

## Slide 54: UNDERSTANDING BINARY LOGIC IS USEFUL
Note that in binary logic the 1st parameter is sequenced as -/+, two parameters as --/++, 3 parameters as ----/++++, etc.. for as many parameters that are measured. The problem encountered after 3 parameters is...how does one visualize the multiple populations?

## Slide 55
A
b
2
A
b
1
A
b
3
A
b
3
A
b
2
A
b
1
A
b
1
A
b
2
A
b
3
c
o
l
o
r
A
b
1
A
b
2
A
b
3
c
o
l
o
r
ne
eg
.
(
-
)
n
e
g
.
(
-
)
n
e
g
.
(
-
)
g
r
e
y
n
e
g
.
(
-
)
n
e
g
.
(
-
)
p
o
s
.
(
+
)
r
u
s
t
o
s
.
(
+
)
n
e
g
.
(
-
)
n
e
g
.
(
-
)
y
e
l
l
o
w
p
o
s
.
(
+
)
n
e
g
.
(
-
)
p
o
s
.
(
+
)
b
l
u
e
ne
g
.
(
-
)
p
o
s
.
(
+
)
n
e
g
.
(
-
)
c
y
a
n
n
e
g
.
(
-
)
p
o
s
.
(
+
)
p
o
s
.
(
+
)
v
i
o
l
e
t
no
s
.
(
+
)
p
o
s
.
(
+
)
n
e
g
.
(
-
)
g
r
e
e
n
p
o
s
.
(
+
)
p
o
s
.
(
+
)
p
o
s
.
(
+
)
r
e
d
COLOR PATTERNS USED TO VIEW COEXPRESSION
Notes: When three antibodies are used together the eight possible combinations of positive and negative cells are shown in the table. When a unique color is assigned to each combination, the position of cells with the same properties generate patterns in the three bivariate plots, representing all the combinations.

## Slide 56
Boolean Logic Table For Four Color Immunophenotyping
Notes: When more than 3 antibodies are used, 16 colors are required. Now there is a practicle problem because we cannot distinguish more than 10 colors with the printers currently used by most flow cytometry labs. A strategy to circumvent this problem is to use 8 colors twice. One antibody is selected as a gating antibody: 3 bivariate distributions using 8 colors for positive cells, for that antibody, and 3 additional bivariate distributions, using the same 8 colors, for negative cells are displayed.

## Slide 57
A
B
C
D
E
F
Ab1
Ab1
Ab1
Ab1
Ab1
Ab1
Ab2
Ab2
Ab2
Ab2
Ab2
Ab2
Types of Antigen Expression
Notes: There are several patterns of antigen expression. The interpretation of them is important for describing the meaning of co-expression. In A, Ab2 is uniformly expressed, while Ab1 is co-expressed by Ab2 cells in a heterogeneous manner. In B, Ab1 is uniformly expressed, while Ab2 is co-expressed by Ab1 cells in a heterogeneous manner. In C, a population of Ab1+Ab2- cells is found, but it is the Ab2+ cells that exhibit heterogeneous expression to produce the Ab1+Ab2+ population. Thus, Ab1 cells are not positive for Ab2. In D, there are two distinct populations: Ab2+Ab1- and Ab2+Ab1+, while in E, the two populations are Ab1+Ab2- and Ab1+Ab2+. In F, correct interpretation can be difficult because this pattern is exhibited by highly autofluorescent cells that are Ab1-Ab2- or dead cells that non specifically bind Ab1 and Ab2. If it is either of these two situations, all combinations of antibodies used will show this pattern on the same percentage of cells. If this pattern represents a true subpopulation of cells it will be unique to the one antibody combination.

## Slide 58
Notes: Interpreting Co-expression: The pattern of expression of two or three markers provides the means for assignment of co-expression. The possibilities are illustrated in this Figure. The antibody combination CD7CD19CD2 was used and in A, B and C the same specimen is shown. CD19 is homogeneously expressed on the cells, as shown in A, but CD7 is expressed in a heterogeneous manner, as shown by a continuum of CD7 expression from negative (cyan) to positive (green). Thus, a proportion of the CD19+ cells express CD7. In B, a small population of CD19+CD2+ cells (violet) is shown. This could be heterogeneous expression of CD2 on the CD19 population, a distinct subset that expresses both markers, or an artifact. Because of this uncertainty, when the frequency of cells co-expressing two or more markers is small, and because the level of confidence increases with increased frequency, we have set a threshold of 10% above which we designate co-expression as real and below which it is uncertain. In this case, the frequency was below 10% of the CD19+ population and we do not know its significance. In C, a distinct subset of CD7+CD2+ cells (blue) is shown which do not express CD19 (A and B): these are normal T-cells. Using a specimen from another patient, in D, non-specific binding is often characterized by events on a 45 degree angle (red) as the antibodies bind equally to all cells. Populations exhibiting this pattern are not included in the interpretation even though they may be greater than 10%.

## Slide 59
THREE OR MORE COLOR
IMMUNOPHENOTYPING
1. IgG Block + MAB
wash
Biotin- second antibody F(ab')2
wash IgG Block + FL- MAB + PE-MAB + TC- Avidin
wash
2. IgG Block + FL-MAB + PE-MAB + B-MAB
wash
TC-Avidin
wash
3. IgG Block + FL-MAB + PE-MAB + TC-MAB wash
TC (third color) = PE/TR or PE/CY5 tandem or PerCP
Notes: 1. Two step reaction, then wash and add a combination of one biotinylated and n directly fluorochrome conjugated antibodies, wash and then add fluorochrome avidin.
2. Add combination of biotinylated antibody with n directly fluorochrome conjugated antibodies, wash and add fluorochrome avidin.
3. Add combination of directly fluorochrome conjugated antibodies.

## Slide 60
STRATEGY FOR SELECTING FLUOROCHROME:
EPITOPE DENSITY
FLUOROCHROME
Low
phycoerythrin, APC
low-intermediate
tandem, CY5
high
fluorescein, PerCP
Notes: Antibodies directed to cellular antigens expressed at low density should be labeled with the brightest fluorochrome whenever possible. Match epitope density with fluorochrome brightness.

## Slide 61: STAINING SOP
50 µl
washed, and
blocked*
whole blood or
bone marrow
15 min. on ice
lyse,
centrifuge,
decant,
blot,
and
resuspend
pellet
wash,
fix,
and
analyse
*add 10 µl mIg (10 mg/ml) to 1 ml washed whole blood.
Add antibody combination
Notes: lysing reagent :
4.13 g Ammonium Chloride (NH4Cl) -- Sigma A-5666
0.5 g Potassium Bicarbonate (KHCO3) -- Sigma P-4913
0.0185 g Tetra Sodium EDTA -- Sigma ED4SS
Add 500 ml double distilled water
Scale quantities for daily use: must be made fresh daily. Use at room temperature. REASON: This reagent must be prepared daily because the dissolved CO2 in water and the buffer combines with NH4CL to form the carbonate (NH4)2 CO3 that is ineffective in lysing erythrocytes. We recommend weighing the reagents and storing them as packets. The dry reagents are dissolved in water as required.
Fix all samples in 0.5 ml of 2% formaldehyde. (Polysciences, cat. # 04018 Ultrapure, E. M. Grade 10% solution. Dilute to 2% in PBS. ) Samples may be run after 30 minutes, however, it is best to wait at least 6 hrs. for the cells’ scatter properties to stabilize. Store fixed cells no longer than one week to avoid increased autofluorescence.

## Slide 62
TANDEM COMPLEX PROPERTIES TO CONSIDER
monocyte binding PE-CY5
light sensitivity PE-CY5
batch variation PE-TR and PE-CY5

## Slide 63: Non-specific Binding to Monocytes
A
B
C
PerCP-CD4
PE-CY5-CD4
FSC
SSC
CD25
CD25
Notes: The PE-CY5 tandem complex binds specifically to myelomonocytic cells. This can result in the misinterpretation of immunophenotypic data using these reagents. In this illustration CD4 binding to monocytes is shown in A, but the PE-CY5 tandem can also bind to monocytes, causing them to appear as bright as lymphocytes (in B).

## Slide 64
TC-CD45
TC-CD3
Effect of Light Exposure on
PE-CY5 Tandem Fluorescence
PE-fluorescence
Notes: Ambient light can cause the PE-CY5 complex to decompose. As CY5 comes off the PE molecules still conjugated to the antibody fluoresce and require increased compensation. Samples that may have been properly compensated at one time, if exposed to light, can become improperly compensated.

## Slide 65: EFFECT OF BATCH VARIATION
PE-fluorescence
Notes: Because there is no industry wide standard for producing tandem complexes, the amount of compensation required will be dependent on the supplier. This can severly compromise immunophenotyping because each company’s reagent will have to be separately compensated. In some cases a different lot of reagent from the same company may require a completely different amount of compensation. Unless properly used, these reagents can produce artifactual, misinterpreted data.

## Slide 66
FSC
SSC
CD16
CD32
CD32
CD64
CD16
CD64
Fc Receptor Expression on Blood Leukocytes
Notes: Fc Receptor Expression on Blood Leukocytes. Human blood was stained with F-CD16 (FcRIII), PE-CD32 (FcRII) and TC-CD64 (FcRI). B cells (cyan) express only CD32, NK cells (orange) express only CD16 and T cells (blue) express no Fc receptors. Monocytes (brown) express both CD32 and CD64 but their position along the CD16 axis and may express low amounts of CD16. Eosinophils (red) are characterized by high side scatter and express about the same level of CD32, but less CD64 and the same CD16 as monocytes and they are also the most autofluorescent cells in the suspension. Both neutrophils (green) and basophils (black) express CD16 and CD32, but not CD64 unless they are activated. Basophils can be resolved from neutrophils because they exhibit low side scatter caused by granules that have a similar refractive index to their cytosol. Thus, not all CD16 binding in the lymphogate is caused by NK cells.

## Slide 67
CD16
CD64
All Cells
CD16
CD64
neutrophils
T-cells
eosinophils
basophils
monocytes
NK cells
B-cells
CD32
CD32
CD32
CD32
Notes: Fc Receptor Expression on Blood Leukocytes.
Each pair of bivariate plots shows the pattern of FcR expression for this hematopoietic cell lineage except the first pair, which is ungated. All populations can be directly resolved based on their Fc receptor fluorescence except basophils and eosinophils. Basophils and monocytes are resolved from neutrophils and eosinophils (high SSC ) using FSC vs SSC in addition to the FcR fluorescence pattern.