## Slide 1: E all'ottavo giorno, Dio creò la citometria (and on the 8th day, God created cytometry)
J. Paul Robinson Professor Purdue University
With thanks to ThermoFisher for sponsoring this Workshop

## Slide 2: Some Commercial Cytometers….
Millipore/Guava
Apogee
Luminex
Accuri
Bryte
BC
BD
BD
BC
BC
BC
Amnis
Bay
Biosciences
BD Influx
BD Aria
Sony
BC
BC
ThermoFisher

## Slide 3: Tyndall 1869
1869

## Slide 4: Andrew Moldavan
It is unclear if Moldavan ever built his cell counter. His short article (less than half a page) describes a number of problems but no results.
Manuscript:
Photo-Electric Technique for the Counting of Microscopical Cells
Andrew Moldavan
Montreal, Canada
Science 80:188-189, 1934
“The purpose of the experiment is to have each microscopical cell passing through the capillary tube, register itself automatically on the photoelectric apparatus, thus creating a micro-current which can be amplified and recorded.”
Moldavan (1934) demonstrates use of a suspending fluid in which were blood cells - the measurements were made in a capillary tube using a photoelectric sensor to make extinction measurements
1934

## Slide 5
1934

## Slide 6
1938
Wallace Coulter
Leaving for Asia to
Sell X-Ray machines for GE

## Slide 7: Historical Overview
Torbjorn Caspersson
1941 - demonstrated that “nucleic acids, far from being waste products, were necessary prerequesites for the protein synthesis in the cell (published in Naturwissenschaften in January 1941) and that they actively participated in those processes.”
1950 - demonstrated that both DNA and RNA increase in actively growing cells famous monograph in 1950 “Cell Growth and Cell Function” described nucleic acid and protein metabolism during normal and abnormal growth. - These studies were made using a Cadmium spark source for a UV light, and primitive electronic circuits for detection of signals.
Used Feulgen stain to stain nuclei
Manuscript:
        Torbjorn O. Caspersson, History of the Development of Cytophotometry from 1935 to the present” in Analytical and Quantitative Cytology and Histology, pp2-6, 1986.

## Slide 8: Fluorescence Labeling Technique
Coons et al 1941 - developed the fluorescence antibody technique - they labeled antipneumococcal antibodies with anthracene allowing them to detect both the organism and the antibody in tissue using UV excited blue fluorescence
Manuscript:
Immunological Properties of an Antibody Containing a Fluorescent Group
Albert H. Coons, Hugh J. Creech and R. Norman Jones
Department of Bacteriology and Immunology, Harvard Medical School, and the Chemical Laboratory, Harvard University
Proc. Soc. Exp.Biol.Med. 47:200-202, 1941
“Moreover, when Type II and III organisms were dried on different parts of the same slide, exposed to the conjugate for 30 minutes, washed in saline and distilled water, and mounted in glycerol, individual Type III organisms could be seen with the fluorescence microscope……”
1941

## Slide 9: Historical Overview
Torbjorn Caspersson
1941 - demonstrated that “nucleic acids, far from being waste products, were necessary prerequesites for the protein synthesis in the cell (published in Naturwissenschaften in January 1941) and that they actively participated in those processes.”
1950 - demonstrated that both DNA and RNA increase in actively growing cells famous monograph in 1950 “Cell Growth and Cell Function” described nucleic acid and protein metabolism during normal and abnormal growth. - These studies were made using a Cadmium spark source for a UV light, and primitive electronic circuits for detection of signals.
Used Feulgen stain to stain nuclei
Manuscript:
        Torbjorn O. Caspersson, History of the Development of Cytophotometry from 1935 to the present” in Analytical and Quantitative Cytology and Histology, pp2-6, 1986.

## Slide 10: Gucker’s Apparatus
A Photoelectronic Counter for Colloidal Particles1
BY FRANK T. GUCKER, J R . , ~ CHESTER T. O’KONSKI,~ HUGH B. PICKARD3 AND JAMES N. PITTS, JR.4
1947
Developed a flow cytometer for detection of bacteria in aerosols
Instrument: Sheath of filtered air flowing through a dark-field flow illuminated chamber. Light source was a Ford headlamp, PMT detector (very early use of PMT)

## Slide 11: Wallace Coulter
Wallace Coulter - Coulter orifice - 1956 -
(patent 1953) - measured changes in electrical conductance as cells suspended in saline passed through a small orifice
The first commercial version of the Coulter Counter
Coulter’s
Original 1953
Patent app’n
From 1949
©J.Paul Robinson
1949
1949 - Coulter WH, US Patent 2,6756, 508.
“Electrical sensing zone method”)

## Slide 12: Conjugated Fluorescein with Isocyanate
Coons and Kaplan (1950) - conjugated fluorescein with isocyanate - better blue green fluorescent signal - further away from tissue autofluorescence. This method used a very dangerous preparative step using phosgene gas
1950

## Slide 13: Early Microfluorometric Scanner Robert Mellors 1951
RC Mellors & R. Silver, A microfluorometric scanner for the differential detection of cells: application to exfoliative cytology, Science 104, 1951
1951

## Slide 14: Marylou Ingram
1951

## Slide 15: P.J. Crosland-Taylor
Sheath Flow Principle – 1952-3
A Device for Counting Small Particles Suspended in a Fluid through a Tube
P.J. Crosland-Taylor
Bland-Sutton Institute of Pathology
Middlesex Hospital, London, W.1. June 17, 1952 Nature 171: 37-38, 1953
“Provided there is no turbulence, the wide column of particles will then be accelerated to form a narrow column surrounded by fluid of the same refractive index which in turn is enclosed in a tube which will not interfere with observation of its axial content.”
1952

## Slide 16
1952
Marylou Ingram in medical school 1944
1960

## Slide 17: Fundamental principle of Sheath Flow PJ Crosland-Taylor
A device for counting small particles suspended in fluid through a tube, Nature 171, 1953 (ref 4756)
An Electronic Blood-Cell Counting Machine, Blood 13, 1958 (ref 40974)
1953

## Slide 18
1953

## Slide 19: Wallace Coulter and Paint!
Lots of stories about Wallace early experiences in developing particle counting
Did he test paint? Was blood a good substitute for paint on a cold evening?
Was be looking for a better way to analyze paint for the navy?

## Slide 20: About Paint Pigments…..
Manufacturing and industrial standards
Before the development of synthetic pigments, and the refinement of techniques for extracting mineral pigments, batches of color were often inconsistent. With the development of a modern color industry, manufacturers and professionals have cooperated to create international standards for identifying, producing, measuring, and testing colors.
http://en.wikipedia.org/wiki/Pigment

## Slide 21: Wallace & The Paint Stories
zinc white iron [prussian] blue
transparent synthetic organics quinacridones phthalocyanines
1um
10um
100 um
chromium oxide green cadmium yellow bismuth yellow titanium white transparent red iron oxides transparent yellow iron oxides
semitransparent synthetic organics arylides
ultramarine blue (GS)
red iron oxides
cadmium red
cadmium orange
semiopaque synthetic organics
diarylides
pyrroles
naphthols
perinone orange
ultramarine blue (RS)
viridian
cobalt blue
violet (brown) iron oxides
yellow iron oxides
cobalt green
cobalt turquoise
cerulean blue
manganese violet
black iron oxides
smallest particles visible without magnification
cobalt violet
manganese blue
coarse historical mineral pigments
modern luster & iridescent pigments
100nm
500nm
1 μm
5 μm
10 μm
50 μm
100 μm
Coulter Counter sensitivity claims
1949-50

## Slide 22: And that story about Navy Paint….

## Slide 24: Watson & Crick-1953
The work which began with Avery's identification of DNA as the "transforming principle" thus led to research that overturned the old conception of DNA as a repetitive and simple molecule, confirmed DNA's role in genetic transmission, and, with James Watson and Francis Crick's 1953 paper, elucidated its structure.
J. D. WATSON and F. H. C. CRICK A Structure for Deoxyribose Nucleic Acid
Nature, 2 April 1953, VOL 171,737 1953
This is a picture of part of the original model built by Watson and Crick at Cambridge in 1953.

## Slide 25: Chicago Operation Moved to New Building
1955

## Slide 26: Hand-drawn advertising drafts of the first Coulter Counter (1956)
1956

## Slide 27
1956

## Slide 28: Brecher Paper on Coulter Counter
1956
Am. J. Clin Path. 26: 1439-1449, 1956

## Slide 29: von Bertalanffy & Bickis - 1956
Ludwig von Bertalanffy (1901--1972)
von Bertalanffy & Bickis (1956)
- the metachromatic fluorescence of AO was used to identify and quantitate RNA in tissues
- also that normal and malignant cells could be discriminated
Absorption Max 467 nm

## Slide 30: Two-Color Cell Counter Patent – RBC & WBC JC Parker and WR Horst 1953
1957

## Slide 31
1957

## Slide 32
1957

## Slide 33
1957

## Slide 34
1959

## Slide 35: 1500 Coulter Counters
1961

## Slide 36: Before Cytometry
Slide Kindly Supplied by Compucyte
Lou Kamentsky – at the IBM’s Watson Labs 1950s and 1960s
1960s

## Slide 37
1962
Valves, Valves and Valves….

## Slide 38
1962

## Slide 39
1962

## Slide 40
1963

## Slide 41: Historical Overview
Early flow systems
Hallermann et al, Kosenow - 1964 - AO staining of leukocytes - was able to use fluorescence (in a flow based system) to select leukocytes from red cells despite a low ratio (1/1000) because they took up lots of AO - also claimed to be able to discriminate between monocytes and PMN
Scan and structure from www.probes.com
Molecular Formula: C17H20ClN3
Molecular Weight: 301.82
CAS Number/Name: 65-61-2 / 3,6-Acridinediamine, N,N,N',N'-tetramethyl-, monohydrochloride
1964
Halleman 1964 AO

## Slide 42: Mort Mendelsohn
CYDAC Analyzer - (1964) - Mendelsohn, Mayall, Prewitt (U.Pen)produced high resolution digital images of leukocytes - cells were stained with gallocyanin chrom alum and naphthol yellow S
Brian Mayall
Early Technology Developers

## Slide 43: Richard Sweet
Richard Sweet developed the electrostatic ink-jet printer which was the principle used by Mack Fulwyler to create a cell-sorter.
1964

## Slide 44: Electrostatic Printing and Droplet Sorting RG Sweet - MJ Fulwyler
RG Sweet, Fluid Droplet Recorder
U.S. Patent 3,596,275
filed 3/25/64 (ref 40975)
MJ Fulwyler, Particle Separator, U.S.
Patent 3,380,584 filed 6/4/65
1965

## Slide 45: Mack Fulwyler
Mack Fulwyler – worked in Marvin van Dilla’s lab at Los Alamos. – developed the sorter in 1965 – initially used electronic cell volume - at Los Alamos National Labs - this instrument separated cells based on electronic cell volume (same principle as the Coulter counter) and used electrostatic deflection to sort. The cells sorted were RBC because they observed a bimodal distribution of cell volume when counting cells - the sorting principle was based on that developed for the inkjet printer by Richard Sweet at Stanford in 1965.
After determining that the bimodal distribution was artifactual, this group were able to sort neutrophils and lymphocytes from blood.
Marvin van Dilla
(Photo dated 6/91)
Mack Fulwyler
Lushbaugh, CC, Basmann,NJ, Glascock, B. Electronic measurement of cellular volumes.
II Frequency distribution of erythrocyte volume. Blood 1962 20:241-248 Correspondence Blood 1964:23:403-405
1965

## Slide 46: The mysterious red cell problem
So it was determined that RBC traveling past the laser were identified as “different” only because of the artifacts developed from the current being too high at the aperture of the coulter counter.
When Fulwyler sorted a single population and reran that population through the Coulter Counter, he again saw the bimodal population proving that the bimodality was an artifact.
As a matter of interest, I spoke to Mack Fulwyler about this experiment, and he told me that the essentially determined the solution to this enormous problem in one afternoon, and after all that, they never actually published a paper about the problem……like good scientists, they just went on to solve a real (biological) problem!!!

## Slide 47: Sorting Cancer Cells - Kamentsky
Spectrophotometric Cell Sorter, LA Kamentsky and MR Melamed, Science 156, 1967 (ref 4134)
1965
Technology was based on a fluidic switched “Typewriter” that IBM was developing in Zurich research laboratories.

## Slide 48: Four Sensors, Sorting, Auto Sampling and Computer Data Reduction
Two analytic instruments were built and one was delivered to LA Herzenberg at Stanford University 1967
IBM 1620 Computer
1966
This instrument became the “Hemalog D” by Technicon in 1974

## Slide 49
1967

## Slide 50
1968

## Slide 51
J.Pharm.Sci 57:557-563, 1968
1968

## Slide 52: Dittrich & Göhde
Dittrich & Gohde - 1969 - Impulscytophotometer (ICP)- used ethidium bromide for a DNA stain and a high NA objective used as a condenser and collection lens
Phywe AG of Gottingen (1969) - produced a commercial version of the ICP built around a Zeiss fluorescent microscope
Laerum, Göhde, Darzynkiewicz (1998)
Photos ©2000 – J.P. Robinson
Göhde and Laerum (1998)
1969
http://www.partec.de/partec/flowmuseum.html
ICP 11 (1969)
Distributed by Phywe, Göttingen
The first commercial flow cytometer
PDP 11 computer

## Slide 53: Herzenberg Lab
Len Herzenberg - 1969 - sorter based on fluorescence (arc lamp) built after working with one of Kamentsky’s RCS systems where they built an instrument they called the Fluorescence Activated Cell Sorter (FACS)
Photos from 2000 – JP Robinson
1969

## Slide 54: Kamentsky & Biophysics Systems
Kamensky’s first benchtop instrument the Cytograph. This measured scatter using a He-Ne laser. This particular instrument was a model prior to the fluorescence detection model.
Kamentsky also built a fluidic cell-sorter to evaluate the cells identified in his RCS. An RCS was sent to Stanford for use by Leonard Herzenberg . The unit was also the model for the Technicon D instrument built by Technicon. (Reference: Shapiro)
©J.Paul Robinson
1970

## Slide 55: Evolution of Leukocyte Gating Strategy for Cluster Subsetting
GC Salzman, JM Crowell, JC Martin, TT Trujillo, A. Romero, PF Mullaney, & PM LaBauve,
Cell classification by laser light scattering: identification and separation of unstained leukocytes,
Acta Cytologica 19, 1975
LR Adams & LA Kamentsky,
Machine characterization of human leukocytes by acridine orange fluorescence, Acta Cytologica 15, 1971
RA Hoffman, PC Kung, WP Hansen,
Simple & rapid measurement of human T
lymphocytes and their subclasses,
PNAS 77, 1980
Lymphocytes
Monocytes
Granulocytes
1971
Biophysics Systems
Los Alamos
Ortho

## Slide 56
1971
Bernie Shoor
BD Internal Memos

## Slide 57
1971
BD Internal Memos

## Slide 58
1971
BD Internal Memos

## Slide 59
1971
BD Internal Memos

## Slide 60
15 Dec 1971
18 Aug 1971
3 Nov 1971
1971

## Slide 61: Stanford Group and BD (Herzenberg) (Agreements made between Nov 3 and Dec 15, 1971 Coulter Group and Particle Technologies (Fulwyler) (Agreements made October 1, 1971)
1971

## Slide 62: Herzenberg & Becton-Dickinson
Herzenberg was the recipient of the very
Prestigious 2006 Kyoto Prize for his work
in development of fluorescence based
flow cytometry. Many people well known
in the field were trained in his lab
(Photo from the official Kyoto Prize website)
1972
Herzenberg -1972 - Argon laser flow sorter - placed an argon laser onto their sorter and successfully did high speed sorting - Coined the term Fluorescence Activated Cell Sorting (FACS) This instrument could detect weak fluorescence with rhodamine and fluorescein tagged antibodies. A commercial version was distributed by B-D in 1974 and could collect forward scatter and fluorescence above 530 nm.
Monday, Sept 6, 2013
Len Passed away Oct 27, 2013

## Slide 63: Herzenberg and Bonner
WA Bonner, HR Hulett, RG Sweet and LA Herzenberg,
Fluorescence Activated Cell Sorting, Review of Scientific Instruments 43, 1972
1972

## Slide 64: Los Alamos and Livermore
Joe Gray sorting chromosomes
Marv Van Dilla and Harry Crissman
Marv Van Dilla and Phil dean
1970s

## Slide 65
Biophysics Systems
Ortho Instruments
Cytograf (1970)
Cytofluorograf (1970)
FC200 (1975)
ELT 8 (1977)
50H (1978)
Spectrum (1979)

## Slide 66: BD Announces FACS-1 April 1974
1974

## Slide 67: FASEB April 1974 – Coulter Booth
1974
Bob Auer head of Coulter’s EPICS division, saw that BD was voing to release their sorter at the FASEB meeting in 1974, so they changed their booth and had their sorter on the booth.

## Slide 68
1974

## Slide 69: EPICS II
1974
Delivered to Chet Herman
NIH in 1974
Coulter developed big multiparameter sorters but Wallace Coulter was in conflict with the idea of building big instruments so he dropped the program. This precipitated Fulwyler to leave Coulter and join BD

## Slide 70: Hemalog D
Technicon - Hemalog D - 1974 - first commercial differential flow cytometer - light scatter and absorption at different wavelengths - chromogenic enzyme substrates were used to identify neutrophils and eosinophils by peroxidase and monocytes by esterase, basophils were identified by the presence of glycosaminoglycans using Alcian Blue - the excitation for all measurements was a tungsten-halogen lamp
Insert photos on page 60
Image from Shapiro “Practical Flow Cytometry”, 3rd. Ed.Wiley-Liss, 1994
1974

## Slide 71: Mack Fulwyler
Coulter Electronics manufactured the TPS-1 (Two parameter sorter) in 1975 which could measure forward scatter and fluorescence using a 35mW argon laser.
This photo (left) is one of only one or two surviving TPS Instruments. It is very similar to the Coulter Counter of the day.
Photo ©2000 – J.P. Robinson
1975

## Slide 72: Monoclonal Antibodies
Georges J.F. Köhler
César Milstein
1975
A photo I took in 1986 at the Cambridge ISAC meeting.
Milstein with is hand in the air (Howard Shapiro on Guitar)
Nobel Prize in Physiology 1984

## Slide 73
Wallace
1975
Wallace Coulter placed this news clipping on Bob Auer’s desk in 1975 after Fulwyler left Coulter to Join Becton Dickinson!! The award was while he was at the Max Plank institute in Germany while he was spending his 1 year sabbatical before he moved to BD.

## Slide 74: Marylou Ingram - 1976
Early adopter of the Coulter Counter technology

## Slide 75: Biophysics -Ortho
Ortho Diagnostics (Johnson and Johnson) purchased Biophysics in 1976 and in 1977 the System 50 Cytofluorograph was developed - this was a droplet sorter, with a flat sided flow cell, forward and orthogonal scatter, extinction, 2 fluorescence parameters, multibeam excitation, computer analysis option.
1979 - NIH scientists had added a krypton laser at 568 nm to excite Texas Red fluorescence at 568 nm and emit at 590-630 nm. Argon (488 nm FITC was measured simultaneously without signal cross-talk - thus the FACS IV was developed (B-D).
FC 200(1975)
System 50H (1978)
1977

## Slide 76: Chromosome Analysis on the TPS-1 Sorter
1977

## Slide 77: Two groups of Lymphocytes B Cells and T Cells….
1977

## Slide 78: Coulter Electronics
1977-78 developed the Epics series of instruments which were essentially 5 watt argon ion laser instruments, complete with a multiparameter data analysis system, floppy drive and graphics printer.
Epics V front end (left) and MDADS (right)
Photo ©2000 – J.P. Robinson
1978

## Slide 79: 1980s and 1990s